## Slide 1: Homework 4 and 5
2020

## Slide 2
Choose in the well log thick sands (one zone only !!) that you assume are brine-saturated sands, use Biot-Gassmann’s formulae to do fluid subtitution in the zone.
  From brine Sw = 100 % (in-situ) to gas - saturated sands Sg = 100 %
  From brine Sw = 100 % (in-situ) to oil - saturated sands So = 100 %
Plot well log results : saturated rock of brine, oil and gas ( use different colours) for Vp, Vs, density. Comment on your results.
Assume
sandstone (incl. clean sandstone and shally sand) GR < 80 API
shale (incl. sandy shale and shale) GR > 80 API
Fluid Properties :
Brine density = 1.10 gr/cc K brine = 2.60 GPa
Gas density = 0.10 gr/cc K gas = 0.02 Gpa
Oil density = 0.80 gr/cc K oil = 1.15 GPa
Rock Properties :
quartz density = 2.65 gr/cc ; K quartz= 37 Gpa; µ quartz = 44 Gpa
Homework 4

## Slide 3
Choose a single point (hi por) in sand reservoirs, assuming the pore space filled with brine, and use Gassman’s fluid substitution to estimate Vp, Vs and density from Sw= 100% & Sgas=0% to Sw= 0% & Sgas=100% with step increment every 2% at a constant porosity.
Similar to no 1, calculate for different fluid content from S w= 100% & S oil=0% to S w= 0% & S oil=100% step increment every 2% at a constant porosity.
Similar to no 1, choose another point (low por) in sand reservoirs and do fluid substitution, from Sw= 100% & S gas=0 % to Sw= 0% & S gas=100 %.
Crossplot between Vp, Vs, Vp/Vs versus % saturated rock. Comment on your results.
Use the following data :
Fluid Properties :
Brine density = 1.05 gr/cc K brine = 2.65 GPa
Gas density = 0.15 gr/cc K gas = 0.05 GPa
Oil density = 0.80 gr/cc K oil = 1.10 GPa
Rock Properties :
quartz density = 2.65 gr/cc ; K quartz= 37 Gpa; µ quartz = 44 Gpa
Homework 5